ST 65-3 CC PROFILE SHEET

The ST 65-3 CC clear anodised aluminium stair nosing is 65mm on the tread with a 50mm PVC insert and a 10mm visible riser, it is suitable for 3mm vinyl floor coverings.

The nosing is designed to be fitted directly to the sub floor that is in good condition (smooth and level/even) with the floor coverings to be cut into the back of the nosing and up the riser which leaves 10mm of exposed nosing down the riser.

The floor coverings must be installed immediately following the installation of the stair nosings otherwise the stair nosings will be a trip hazard.

End Caps are NOT available.

Drilled at approximately 250mm spacings.

Slip Test Results with PVC insert = P4

We recommend you seek the certifier’s approval on the profile and insert colour as they all interpret the standards differently.