ST 74 SN PROFILE SHEET

The ST 74 SN clear anodised aluminium stair nosing is 75mm on the tread with a 50mm pvc insert and has a 10mm riser.

Please Note: The underside of the riser is only 5mm.

Adhesive to be used under the stair nosing when fitting directly to the subfloor (Adhesive NOT supplied for a supply only)

Designed to be fitted direct to concrete or timber or over resilient floor coverings.

Not suitable for soft floor coverings.

The sub floor must be in good condition (smooth, level & clean) and the head of the steps must be square fronted.

End Caps are NOT available.

Drilled at approximately 250mm spacings or can be supplied in blank form.

Slip Test Rating = P4

We recommend you seek the certifier’s approval on the profile and insert colour as they all interpret the standards differently.